## Slide 1
Review OQC sampling method
Case 1 : OQC pick up sample before ID pallet  Return to ID pallet station
( ID pallet station : Reading Inner carton S/N - Outer carton S/N  issue ID pallet )
 No risk for wrong packing inner box S/N and outer box S/N
 Need to review OQC area how to control Product S/N and Inner carton S/N
Case 2 : OQC pick up sample after issue ID pallet ( Ratio : 2% )
Assy
ID Pallet station
Packing
OQC
OQC
FA warehouse
Case 1
Case 2 : For HC400 serries
ID pallet issue in FA process
SCM warehouse
Shipment
Pickup sample
Record ID pallet
OQC sampling check
Return to SCM W/H
Step 2: Matching ID pallet and Outer
carton before return
Step 1: Recorded ID Pallet and
S/N carton box by excel file
No risk for return wrong pallet
Need to review OQC area how to control Product S/N - Inner carton S/N – Outer S/N

## Slide 2
Review control sample at OQC area ( System control )
Pick up sample
Reading barcode Inner/Outer
Reading barcode
Inner/Outer
Confirm S/N Outer & all inner boxes
Return to Pallet
Weight check 1st
Weight check 2nd
Reliability
OQC
inspection
Reading BC
Product / Inner
Numbering control & Separate area
Confirm S/N Outer & all inner boxes
Product / Warranty/ Manual & Inner box
Accessory control
Accessory control
*In case not matching Product / Warranty/ Outer & Inner  Can find out before packing
Physical control
1person – 1 model
– 1 table
Same time inspection
Reliability test area separate control and clear indication
After reliability test , product return to check full OQC item

## Slide 3
Note: Model not have S/N  Control as current method
FA
Shipment
- Weight check
- Pro date/Model/Q’ty
- Issue FG control sheet
Pallet ID
SCM
① Add OQC :
Input sampling plan
Input Sampling product & Serial No
② Indication OQC situation:
Input Sampling result
Input total judgment All lot.
 Send result by Email auto
- Issue Pallet ID: Model/Q’ty/SN
- Issue Movement slip <SAP>
- Read Pallet ID Model/Q’ty>
- Take out FG control sheet>
- Compare FG & WMS
- Read Pallet: <Model/Q’ty>
- Take out FG control sheet
- Compare FG & WMS
③ QC inspection result:
Reading Pallet ID to check OQC result
Indicate OK lot
④ Function: If OQC judgment NG or Not yet
Stop next step
< PSNV/ Jupiter >
Study to link weight check & WMS
Save:
8,000min/month
4000 paper
Save:
Reduce 2pax
990H/year
Save:
4,000 min/month
CURRENT SITUATION
Additional
Additional
Additional
Additional
- Sampling pick up
REQUEST
MERIT
OQC
Project: Link weight check system FA-SCM-OQC

## Slide 4
◆ After
OQC Issue
Risky point : Wrong packing pass to market by control offline
Loss time to confirm production result & Shipment schedule : 90sec*150lots=3.75H/day.
2pax/ day need to follow chop stamp in warehouse.
Improvement: Link system from FA-OQC-SCM
Prevent wrong packing.
Save time : 3.75H/day ~ 990H/year
Save manpower : △ 2pax for stamp ~ 12K$/ year
◆Before
FA
OQC
SCM
. No indicate shipment priority
. No indicate result timely
. Cannot use weight system  compare S/N by manual
. Update OQC result not timely.
. Loss time to come to SCM for chop stamp.
. Loss time to confirm stamp by visual check
2pax
FA
OQC
SCM
. Indicate result timely
. Indicate shipment priority
. Use weight system  auto compare S/N
. Online update OQC result & Save time to come to SCM for chop stamp
. No need check stamp by visual
. Confirm OQC result by system
Target improve:
Prevent wrong packing leakage out to market
△ 2pax for stamp by manual
Link
Link
1/1
Project: Link weight check system FA-SCM-OQC

## Slide 5
OQC DIGITAL SYSTEM
1
2
3
4
5
6
7
8
Steps
9
12
13
11
14
OK
NG
10
Notify NG error for FA
Find Pallet ID & F/G
Matching Pallet ID & Outer carton
Record Pallet ID & S/N carton
Find all lots same model, shift, date, line
Chop stamp physical all lots
Report daily
Second check
First check
OQC inspection
Check S/N inner product
Weight 2nd
Return sample
Pick up sample
OQC inspection
OQC chop stamp procedure
Overview of the OQC inspection process
OQC inspection result no link FA & SCM system, easy mistake. (7 steps)
All procedures are manual by Excel, loss time to traceability, and skip processes.
The results of the inspection process are manually stamped. Loss of time to stamp.
2