## Slide 1
Link weight check system concept
1

## Slide 2
Production
OQC visualize system
Link weight check system concept
Shipment
PEM system
Record 4M change
Process quality issue
Weight check system
Production result
Link with ID pallet system
Shipment request (Priority)
Purpose
Indicate process 4M/ Quality each Lot
Visualize OQC checking status
Indicate shipment permission
Trace back for Market feedback
ADD
ADD
ADD
VMS system
Visualize status of model following shipment plan daily
Link final confirmation to WMS/PDA
ADD
ADD
Advantage
Remove manual Job FA/OQC/SCM
Eliminate human risk & follow up quality /4M issue to evaluate LOT
Visualize shipment permission timely
Production : △… H
SCM : △… H
Visualize OQC inspection result
QC : △2pax
PEM
System
Weight check
System
VMS
System
OQC system
Link
Link
Link
ID pallet
Shipment
Auto system replace manual Job and visualize quality /4M information to evaluate Lot for shipment

## Slide 3: Defect system

## Slide 4
Manual find location to kitting
Manual record OUTPUT qty to stock card
Manual control FIFO when kitting
Manual control kitting position
Receiving is not indicated on SAP
Manual print receiving card manual find & paste
Manual back flush
① RECEIVING
② STORING
③ KITTING
④ SUPPLY
3.Add barcode
direct print
receiving card
Vendor
SMART WAREHOUSE MANAGEMENT CONCEPT
CURRENT
AFTER
- Free
location rack
- E-map
control
❹
Manual control position by Excel file
Manual find location to store
Manual record INPUT qty to stock card
Manual transfer on SAP another store
Manual Auto control position by E-map
Manual Auto find location to store
Manual Scan INPUT qty to unit barcode
Manual Auto transfer on SAP another store
Manual Auto find location to kitting
Manual Scan OUTPUT qty to unit barcode
Manual control FIFO by system
Manual Control kitting position by E-map
Receiving is not indicated on SAP
Manual Auto print receiving card manual find & paste
Manual Auto back flush
Proposal
Auto transfer
Manual find trolley
put material
Auto transfer
Manual Auto find trolley put material
J.I.T area
6 a.m
7 a.m
8 a.m
Prepare OK
Kitting
Kitting
Kitting E-map [New]
Storing E-map [New]
1/3
FA line
Free Receiving
[Done FY22]
Data synchronization
❸
Auto transaction
Add mobile printer
Auto backflush
E-map kitting
❺
❶ ❷ ❸
❸ ❹ ❺
❸ ❹


Inhouse
(PMD/OCS/FA)
FOSS

E-map trolley
Need storing
No-storing
Sub material
J.I.T
non inspection
inspection
FA sub
Material centralize
❷
FOSS
Control
inventory
Storing part
HC
reduce
∆2pax
∆4pax [LFC: ∆2pax]
∆8pax [LFC: ∆5pax]
∆1pax
∆15pax [LFC: ∆10pax]
JIT
1.Have barcode max 80%
2.No barcode 20%
(New supplier/cost up)
❶
FOSS classify
FOSS classify
FOSS classify
direct print
Part card
[New]

## Slide 5
OQC: Manual find pallet
FA/SCM: Manual confirm Pallet status
OQC manual control sample: Q’ty, serial No ..
FA not know box OQC pick up
① Pick up sample
② OQC inspection
③ Chop stamp
④ Shipment
Manual control weight check
Not update inspection result
Manual make report
Manual confirm product lot status
WMS
Database server
FA warehouse
(E-map control)
FA create Pallet ID
Weight check FA
OQC
Pick sample
Return sample
FA In/Out location
Visualize OQC inspection result
OQC Judge
SCM warehouse
CURRENT
NEW SYSTEM
AFTER
Link weight check system concept
System indicate S/N OQC pickup & inspection progress
System indicate OQC & Lot judgment
Eliminate manual job OQC
 Save: 1,000H/year
E-chop and indication on system
FA: Save 213.4$/year
OQC: ∆2pax
E-chop and indication on system
SCM: Save 800H/year
1
OQC inspection

## Slide 6
Project members
2
Hien IT
Project Manager
Minh IT
Project Leader
OQC
Member
FA
Member
SCM
Member
Add
Member

## Slide 7
Sept W3
Sept W4
W1.Oct
W2.Oct~
Nov
Dec
Jan.25
Project 01
11/9/2024
Project Establishment &
Environment Preparation
Project 02
23/9/2024
Project 03
1/11/2024
Project 04
1/12/2024
Project 05
20/1/2025
Project plan & Approve
Concept scope confirm
Functions confirmation
Unit Test
SIT
UAT
System design & develop
Functions confirmation
Unit Test
GO-LIVE
Project Schedule
3
Notes: KH cũ: 12,1,2,3.2025

## Slide 8
Details of OQC pickup sample & chop stamp
Production plan
Pick up sample
OQC Normal inspection
Reading barcode Product / Inner
Weight check 2nd
Reading barcode Inner/Outer 2nd
Return to Pallet
Reading barcode Inner/Outer 1st
Weight check 1st
Find Pallet ID&F/G
Matching Pallet ID & Outer carton box
Record Pallet ID & S/N carton
Find all lots same model, shift, Line
Chop stamp physical all lots
Report daily
PCS issue Pro plan
①
②
③
④
⑤
⑥
⑦
⑧
⑨
⑩
Reliability
inspection
⑪
⑫
⑬
⑭
⑮
⑯
FA
ID pallet
FA
warehouse
Scan ID pallet to receive by PDA
Confirm receiving by WMS
⑰
⑱
⑲
⑳
OQC pick up & Return sample
OQC chop stamp
FA/SCM
SCM shortage
FA confirm stock
Details current procedure from PCS  FA  OQC  SCM
Current situation:
Pickup & Return sample  Manual Job at process: ① ~ ⑦
Chop stamp: Loss time to find pallet  Manual Job at process: ⑪ ~ ⑯
Need to improve
4

## Slide 9
Step 1: SCM send inventory & shipment plan
Step 2: FA update inventory & shipment plan
① Confirm shortage shipment
◆ Proposal
◆ Current
Indicate priority shipment model to announce OQC pick up inspection
Indicate details: Ship by Board/Air, Stock Q'ty, shipment Q’ty, Minus product compare vs shipment plan
Minus product: Q’ty, Reason, when re-running (need indicate)
In case production plan be changed  Auto refresh
Classify type of product and display : EMC, PP, PMP and can shipment or not (Ex: PP cannot shipment..)
Using time: 5 mins/day*4 BD/BU =20 mins/day
Save time: 20 mins/day
OQC confirm shipment plan to focus priority shipment models by manual
Step 3: OQC input shipment info to focus check priority
Request system will be displayed details:
5
IT confirm: Hưng Đạo sẽ trả lời về lấy dữ liệu hàng thiếu (SCM xác nhận tiếp)
 OQC cấp IT file của OQC hnay (excel chi tiết)  4-OCt

## Slide 10
Step 2: OQC copy into OQC format to control
Step 1: PCS send Daily production plan <Email/Server>
① OQC re-make production plan
OQC re-making production base on information of PCS:
Add some information: Sample Q’ty, PL, Characteristic, Reliability, Specification…
 Using time: 10 mins/day
System will link with OQC inspection plan and auto update:
 Save time: 10 mins/day
OQC re-making production plan base on production plan that PCS send
◆ Proposal
◆ Current
OQC make database: Sample Q’ty; Reliability plan
System will be linked with OQC Inspection plan:
OQC sampling Q’ty (Incase if happen Quality issue, sample Q’ty level will be changed  Return to previous level  OQC make Data base)
Add : 1 column for adjust sample if need to follow up quality issue
Auto assign model that should be Reliability test
Auto change sample Q’ty level (Ex: Normal level  Loosen level)
If cannot catch up plan  Can adjust and display reason (Only OQC member can revise)
Q’ty sample Standard
Plan
Plan
6
 OQC cấp IT file của OQC đang làm hiện tại (excel chi tiết)  3-OCt

## Slide 11
② OQC pick up sample
Scan barcode of Outer box  Displays Outer box OQC pick up: FA easy to control sample quantity OQC pick up
System will remind OQC to pick up sample
Indicate time OQC pick up sample on system
Indicate pallet OQC pick up sample to eliminate finding and scan barcode many times
Using time: 1mins*8 times/day=8 mins/day
Save: 8 mins/day
OQC pick up sample follow serial range
◆ Proposal
◆ Current
Step 1: Access PSNV Portal to confirm Production result
Step 2: Divide serial range to pick up sample at Pallet
Pick up outer box & put indication
DP
Pick up inner box & put indication
DECT
System can be indicated:
7

## Slide 12
③ Reading barcode Inner/Outer 1st time
Using time: 30lots*10sec*2Outer boxes=10mins/day
Save: 10 mins/day
Confirm Outer carton and inner box
◆ Proposal
◆ Current
Reading Barcode of Outer box and Inner box
System link weight check system to confirm Outer box includes which inner boxes
8
Purpose: To confirm Outer box includes how many inner box and which serial No

## Slide 13
④ Weight check 1st time
Using time: 150pcs*5sec*2 BD/BU=24mins/day
Save: 24 mins/day
Weight check offline at OQC to confirm accessory
◆ Proposal
◆ Current
Weight check 1st time (Control offline):
System link weight check system to weight of inner box
9
FA already applied weight check system: No need add this point  No need do weight check 1st at OQC
Purpose: To confirm full inner box before un-packing

## Slide 14
⑤ OQC Normal inspection
OQC normal inspection
◆ Proposal
◆ Current
After OQC finish inspection  System indicate result of each serial No (In case NG will be indicated NG situation and reason NG)
System auto confirm matching sample Q’ty with database to indicate changing situation
+ System alarm if inspect duplicated serial No
+ Save history of sample check  Can Traceability
Incase FA happen quality issue  How to indication on system (Prevent OQC judgment OK when FA happen NG)  How to return product of this lot?
System link with Database sample Q’ty:
Appearance check
Function check
Confirm the number of samples to be taken
Manual confirm sample Q’ty enough or not
Current inspection procedure
10
Nếu số lượng còn lại của lô mà phát sinh NG thì hệ thống báo FA kết thúc sản xuất để OQC judgment cả lô

## Slide 15
⑥ Reliability inspection
Reliability inspection:
◆ Proposal
◆ Current
OQC make Database about grouping series model need to check Characteristic, Reliability (Monthly)
System auto select model and remind to inspect:
+ Limit Q’ty of model to be suitable with OQC lead time
(For Ex: OQC can check 2pcs characteristic)
+ System default: After Reliability test  Normal inspection.
In case sample not yet checked normal  Will be alarm
+ In case happen Quality issue will be displayed NG situation
and after rework/repair  Change situation (Have history:
Main cause, action)
+ If the model only produced 1 time in a month  Need to
indicate in inspection plan
Basic function check: Power ON check
Inspect: Characteristic, Specification, Reliability
Confirm checking plan of characteristic, specification, reliability
Full function check
System link with Database sample Q’ty:
Indicate result in OQC control sheet
Current inspection procedure
11
Bổ sung thêm nội dung vào trang đánh giá lô

## Slide 16
Reading barcode Product Inner to confirm correct S/N
⑦ Reading barcode Product Inner to confirm correct serial No
OQC make master list product ingredients: Monitor, camera, wireless, charger…
System can auto indicate ingredients must read barcode
Link with FA system to confirm ingredients inside?
This process is re-packing:
+ How to indicate set by set inspection result ?
NG or OK ? Any problem happen ?What is next action ?
+ How this result link to total Judgment ?
Confirm ingredients of product for ensure matching Serial No
◆ Proposal
◆ Current
Reading barcode Product Inner to confirm correct S/N
12
Gửi file excel mẫu và master list: 4-OCt

## Slide 17
⑧ Weight check 2nd time
Current procedure from PCS  OQC  FA  SCM
◆ Proposal
◆ Current
Weight check 2nd time:
Purpose: To confirm full inner box after packing, compare weight check 1st time & 2nd time for judgment
Weight check 2nd time: Auto link with weight check system of FA to compare weight of inner box and Judgment
FA weight check system
Link
13
How can detect if FA weight check system have trouble ?

## Slide 18
⑨ Reading barcode Inner/Outer 2nd time
Confirm matching Outer box with inner box
◆ Proposal
◆ Current
Scan ID outer  Auto link with FA weight check to compare Outer box & inner box
Reading barcode Outer & Inner 2nd time
Purpose: Ensure correct Outer box & Inner box
System auto link with FA weight check system
FA weight check system
Link
14

## Slide 19
⑯ Output check sheet inspection & Report
 Using time: 10 mins/day
Save time: 10 mins/day
Record OQC inspection check sheet and report
◆ Proposal
◆ Current
System auto output: Production Q’ty, Serial range, FA line, Production date, OQC sample serial No, Inspection date, Sample Q’ty
When reading barcode to start inspection : System link and open OQC check sheet. Then OQC check 1pc complete and indicate OK  Link to system for inspection result
Auto output inspection check sheet (Pdf) follow inspection date, lot
System auto output OQC inspection result
Current situation:
Manual making OQC inspection check sheet:
Manual input summary OQC inspection result:
15
Gửi file form báo cáo mẫu: 4-Oct
(Đặc tính, đối chiếu?)

## Slide 20
⑪~⑮ OQC chop stamp
Current chop stamp procedure
Using time:
DP/Dect: 480 mins/day
MW/TV/PJ/SB/PAPVN: 480mins/day
Save time: 960 mins/day ~ 2pax
◆ Proposal
◆ Current
Indicate Judgment lot on system  All sections can understand lot situation
Eliminate physical chop stamp
How system link with ID pallet station or how to prevent production move to SCM without OQC approval ?
System auto indicate judgment lot
Current situation:
Finding pallet to confirm correct model, Q’ty
Read ID Pallet & S/N carton box by excel file
OQC find Pallet ID
Matching ID Pallet and Outer Carton
Find all same model, production date, line, shift
OQC chop stamp all ID Pallet
OQC
OK
DD-MM-YY
Chop stamp on Pallet sheet
16
Đối với các pallet OQC đóng dấu thì FA sẽ kéo ra và để ở khu vực gần thang máy, nếu OK cả lô thì mới cho vào thang máy

## Slide 21
Rule to Judge 1 LOT
17
1st sample
2nd sample
N sample
……
OK
OK
OK
Final Judgment for Lot
OK
Identify 1 lot:
There is another model to insert running while current model is running  Switching model time is counted a new lot (Lot: Change another model or finish working shift)
Judgment 1 lot:
OQC will judge lot after finish inspection all sample Q'ty regardless of whether production has ended  THêm điều kiện: OQC finish sample Q’ty + FA finish production
Làm rõ, bổ sung

## Slide 22
OQC DASH BOARD
Visualize status of Lot
Indication location at warehouse
OK
Checking
NG
Not checked yet
Checking
<Can move pallet>
Status situation
Not checked yet : OQC not taken sample yet
Checking : Under OQC checking
Checking : Under OQC checking (Sample Q’ty already checked over a half Q’ty of all sample)
<Can move pallet>
OK : All Lot judgment OK
NG : Lot judged NG
OQC inspection indication
Location indication at warehouse
18
How to control non-inspection pallet ?
Need to decide rule to transfer OK lot to SCM

## Slide 23
Preparation Equipment for system
Equipment list up (OQC)
19
Cat/Equipment |  | DP/DECT | MW | PJ/SB | TV
Tablet (Connect with barcode reader) | Available (pcs) | 1 | 1 | 0 | 0
 | Additional (New) (pcs) | 1 | 0 | 1 | 1
 Need to add more 3pcs tablet
FA: xác nhận PDA=?pcs

## Slide 24
Currently
Manual check OQC display OK
Manual transfer F/G to SCS (SAP system)
Printing hard movement slip: 3600pcs/monthly  7.2Ream
Cost: 7.2*2.47$ = 17.78$/month ~ 213.4$/Year
Improvement
Check OQC OK by PDA
Auto transfer F/G to SCS (SAP system)
Abolish hard movement slip: 7.2Ream
Save Cost: 213.4$/Year
BEFORE
AFTER
FA
Reduced : 213.4 S/Y
Current process
Print movement slip
Manual check OQC OK
Production F/G OK
FA Make ID ID pallet
OQC stamping OK on slip sheet
Waiting OQC check
FA transfer SCS (SAP system)
FA transfer SCS (Actual)
OQC OK
Download ID pallet scaned
Print movement slip
Production F/G OK
FA Make ID ID pallet
OQC stamping OK on System
Waiting OQC check
Auto transfer
SCS (SAP system)
FA transfer SCS (Actual)
OQC OK
Download ID pallet scaned
Improvement process
OQC OK
Check OQC OK by PDA
LINK
SCS Receive the finish goods Scan ID Pallet Code
Change method transfer F/G to SCS
20

## Slide 25
OQC DIGITAL SYSTEM LINK WMS & CONFIRMATION DATA
DASHBOARD
SCS request:
Visualize status of model following shipment plan daily
Link final confirmation to WMS/PDA for operator working in warehouse
LINK WMS/PDA
FA
SCS
OQC
Finish production
Pallet ID finish
Judgement OK
Sampling inspection
Judgement OK
Scan ID pallet to receive
Confirm receiving
SCS check all data by download
**
Scan ID pallet
Email auto
Result NG
Confirm data PDA
FA/QC recheck
Shipment plan
*
②
①
Shipment plan
Result judged OK
③
*
**
③
Dashboard
PSNV Portal
“Control shipping plan”
WMS
Judgement auto email
FA transfer cargo to SCS
Option 1
Option 2
Warning to dashboard
SCS visualize on pallet
①
WMS
Dashboard
Confirm receiving
Format check
Auto update
SCM
21

## Slide 26
FORMAT DOWNLOAD FROM DASHBOARD
Details shortage shipment plan daily on WMS
Shortage shipment plan daily on WMS
OQC DIGITAL SYSTEM LINK WMS & CONFIRMATION DATA
22