## Slide 1
Review OQC pickup sample & chop stamp
Production plan
Pick up sample
OQC Normal inspection
Reading barcode Product / Inner
Weight check 2nd
Reading barcode Inner/Outer 2nd
Return to Pallet
Reading barcode Inner/Outer 1st
Weight check 1st
Find Pallet ID&F/G
Matching Pallet ID & Outer carton box
Record Pallet ID & S/N carton
Find all lots same model, shift, Line
Chop stamp physical all lots
Report daily
PCS issue Pro plan
①
②
③
④
⑤
⑥
⑦
⑧
⑨
⑩
Reliability
inspection
⑪
⑫
⑬
⑭
⑮
⑯
FA
ID pallet
FA
warehouse
Scan ID pallet to receive by PDA
Confirm receiving by WMS
⑰
⑱
⑲
⑳
OQC pick up & Return sample
OQC chop stamp
FA/SCM
SCM shortage
FA confirm stock
Current procedure from PCS  FA  OQC  SCM
Current situation:
Pickup & Return sample  Manual Job at process: ① ~ ⑦
Chop stamp: Loss time to find pallet  Manual Job at process: ⑪ ~ ⑯
Need to improve
1

## Slide 2
Step 1: SCM send inventory & shipment plan
Step 2: FA update inventory & shipment plan
① Confirm shortage shipment
◆ Proposal
◆ Current
Indicate priority shipment model to announce OQC inspection
Indicate details shipment plan: Time, Board/Air
Indicate stock Q'ty, shipment Q’ty
How to control minus product: when re-running
In case production plan be changed --> How to control ?
Using time: 5 mins/day*4 BD/BU =20 mins/day
Save time: 20 mins/day
OQC confirm shipment plan to focus priority shipment models
Step 3: OQC input shipment information to focus check priority
System will display details:
2

## Slide 3
Step 2: OQC copy into OQC format to control
Step 1: PCS send Daily production plan <Email/Server>
① OQC re-make production plan
OQC re-making production base on information of PCS:
Add some information: Sample Q’ty, PL, Characteristic, Reliability, Specification…
 Using time: 10 mins/day
System will link with OQC inspection plan and auto update:
 Save time: 10 mins/day
OQC making production plan base on production plan that PCS send
◆ Proposal
◆ Current
Step1: OQC make database: Sample Q’ty; Characteristic/Reliability plan
System will be linked with OQC Inspection plan and indicate details:
OQC sampling Q’ty
Assign model that will be Reliability test
Auto change sample Q’ty level (Ex: Normal level  Loosen level)
Testing Frequency:
Characteristics/Specification : 1pcs/series model/month
Reliability test: 3pcs/series model/3 months
Standard
Plan
Plan
3

## Slide 4
② OQC pick up sample
Scan barcode of product  Displayed OQC sample Q'ty (System auto indicate sample Q’ty
Indicate lot number (Auto change sample level)
Reminder the time to pick up sample: Divide Serial No range to pick up sample
Using time: 1mins*8 times/day=8 mins/day
Save: 8 mins/day
OQC pick up sample follow serial range
◆ Proposal
◆ Current
Step 1: Access Portal to confirm Production result
Step 2: Divide serial range to Pick up sample at Pallet on FA line
Pick up outer box and put indication
DP
Dect
Pick up inner box and put indication
Dect
System can be indicated:
4

## Slide 5
③ Reading barcode Inner/Outer 1st time
Using time: 30lots*10sec*2Outer boxes=10mins/day
Save: 10 mins/day
Confirm Outer carton and inner box
◆ Proposal
◆ Current
Reading Barcode of Outer box and Inner box
Purpose: To confirm Outer box includes how many inner box and which serial No
System link weight check system to confirm Outer box includes which inner boxes
5

## Slide 6
④ Weight check 1st time
Using time: 150pcs*5sec*2 BD/BU=24mins/day
Save: 24 mins/day
Weight check offline at OQC to confirm accessory
◆ Proposal
◆ Current
Weight check 1st time:
Purpose: To confirm full inner box before un-packing
System link weight check system to weight of inner box
 Weight already recorded weight of inner box
 No need do weight check 1st at OQC
6

## Slide 7
⑤ OQC Normal inspection
OQC normal inspection
◆ Proposal
◆ Current
OQC make Database sampling of model  System auto link to Database to indicate sampling Q’ty of model
After finish inspection  System indicate result of each serial No  Matching sample Q’ty with database to indicate changing situation
System link with Database sample Q’ty:
Appearance check
Function check
Confirm the number of samples to be taken
Manual confirm sample Q’ty enough or not
Current inspection procedure
7

## Slide 8
⑥ Reliability inspection
Reliability inspection:
◆ Proposal
◆ Current
OQC make Database about grouping series model need to check Characteristic, Reliability  System auto select model and remind to inspect
Limit Q’ty of model to be suitable with OQC lead time
System alarm if inspect duplicated serial No
Basic function check: Power ON check
Inspect: Characteristic, Specification, Reliability
Confirm checking plan of characteristic, specification, reliability
Full function check
System link with Database sample Q’ty:
Indicate result in OQC control sheet
Current inspection procedure
8

## Slide 9
Reading barcode Product Inner to confirm correct serial No
⑦ Reading barcode Product Inner to confirm correct serial No
OQC make master list product ingredients: Monitor, camera, wireless, charger…
System can auto indicate ingredients must read barcode
Confirm ingredients of product for ensure matching serial No
◆ Proposal
◆ Current
Reading barcode Product Inner to confirm correct serial No
9

## Slide 10
⑧ Weight check 2nd time
Current procedure from PCS  OQC  FA  SCM
◆ Proposal
◆ Current
Weight check 2nd time:
Purpose: To confirm full inner box after packing, compare weight check 1st time & 2nd time for judgment
Weight check 2nd time: Auto link with weight check system of FA to compare weight of inner box and Judgment
FA weight check system
Link
10

## Slide 11
⑨ Reading barcode Inner/Outer 2nd time
Confirm matching Outer box with inner box
◆ Proposal
◆ Current
Scan ID outer  Auto link with FA weight check to compare Outer box & inner box
Reading barcode Outer & Inner 2nd time
Purpose: Ensure correct Outer box & Inner box
System auto link with FA weight check system
FA weight check system
Link
11

## Slide 12
⑯ Output check sheet inspection & Report
 Using time: 10 mins/day
Save time: 10 mins/day
Record OQC inspection check sheet and report
◆ Proposal
◆ Current
System auto output: Production Q’ty, Serial range, FA line, Production date, OQC sample serial No, Inspection date, Sample Q’ty
System auto output OQC inspection result
Current situation:
Manual making OQC inspection check sheet:
Manual input summary OQC inspection result:
12

## Slide 13
⑪~⑮ OQC chop stamp
Current chop stamp procedure
Using time:
DP/Dect: 480 mins/day
MW/TV/PJ/SB/PAPVN: 480mins/day
Save time: 960 mins/day ~ 2pax
◆ Proposal
◆ Current
Indicate Judgment lot on system  All sections can understand lot situation
Eliminate physical chop stamp
System auto indicate judgment lot
Current situation:
Finding pallet to confirm correct model, Q’ty
Read ID Pallet & S/N carton box by excel file
OQC find Pallet ID
Matching ID Pallet and Outer Carton
Find all same model, production date, line, shift
OQC chop stamp all ID Pallet
OQC
OK
DD-MM-YY
Chop stamp on Pallet sheet
13

## Slide 14
Rule to Judge 1 LOT
14
1st sample
2nd sample
N sample
……
OK
OK
OK
Final Judgment for Lot
OK
Identify 1 lot:
There is another model to insert running while current model is running  Switching model time is counted a new lot (Lot: Change another model or finish working shift)
Judgment 1 lot:
OQC will judge lot after finish inspection all sample Q'ty regardless of whether production has ended

## Slide 15
OQC DASH BOARD
Visualize status of Lot
Indication location at warehouse
OK
Checking
NG
Not checked yet
Checking
<Can move pallet>
Status situation
Not checked yet : OQC not taken sample yet
Checking : Under OQC checking
Checking : Under OQC checking (Sample Q’ty already checked over a half Q’ty of all sample)
<Can move pallet>
OK : All Lot judgment OK
NG : Lot judged NG
OQC inspection indication
Location indication at warehouse
15

## Slide 16
Preparation Equipment for system
Equipment list up (OQC)
16
Cat/Equipment |  | DP/DECT | MW | PJ/SB | TV
Tablet (Connect with barcode reader) | Available (pcs) | 1 | 1 | 0 | 0
 | Additional (New) (pcs) | 1 | 0 | 1 | 1
 Need to add more 3pcs tablet

## Slide 17
Proposal Procedure PCS  FA  OQC  SCM
Production plan
Pick up sample
OQC Normal inspection
Reading barcode Product / Inner
Weight check 2nd
Reading barcode Inner/Outer 2nd
Return to Pallet
Reading barcode Inner/Outer 1st
Weight check 1st
Report daily
PCS issue Pro plan
①
②
③
④
⑤
⑥
⑦
⑧
⑨
⑩
Reliability
inspection
⑯
FA
ID pallet
FA
warehouse
Scan ID pallet to receive by PDA
Confirm receiving by WMS
⑰
⑱
⑲
⑳
OQC pick up & Return sample
Auto judge Lot on system
FA/SCM
SCM shortage
FA confirm stock
Proposal procedure from PCS  FA  OQC  SCM
Merit:
OQC manual Job : Save 92 mins/day
OQC save man power : 2 pax
17