## Slide 1
Details of OQC pickup sample & chop stamp
Production plan
Pick up sample
OQC Normal inspection
Reading barcode Product / Inner
Weight check 2nd
Reading barcode Inner/Outer 2nd
Return to Pallet
Reading barcode Inner/Outer 1st
Weight check 1st
Find Pallet ID&F/G
Matching Pallet ID & Outer carton box
Record Pallet ID & S/N carton
Find all lots same model, shift, Line
Chop stamp physical all lots
Daily Report
PCS issue Pro plan
①
②
③
④
⑤
⑥
⑦
⑧
⑨
⑩
Reliability
inspection
⑪
⑫
⑬
⑭
⑮
⑯
FA create
ID pallet
FA
warehouse
Scan ID pallet to receive by PDA
Confirm receiving by WMS
⑰
⑱
⑲
⑳
OQC pick up & Return sample
OQC chop stamp
FA/SCM
SCM shortage
FA confirm stock
Jupiter
Details current procedure from PCS  FA  OQC  SCM
Current situation:
Pickup & Return sample  Manual Job at process: ① ~ ⑦
Chop stamp: Loss time to find pallet  Manual Job at process: ⑪ ~ ⑯
Need to improve
1
Shipment
(21)
(22)

## Slide 2
Flow chart from OQC  FA  SCM  Jupiter
Note:
Pallets that OQC not pickup sample  Can be transferred to SCM warehouse but are still in checking status on OQC system
SCM need to control product under “Checking status” for ensure not ship out to Market
These pallets can be transferred to Jupiter & Jupiter must be linked to OQC system to know whether product status is OK or not
4
OQC Visualize System
SCM
out location
Ship to
Market
SCM Warehouse
FA
fix location
OQC return sample
Jupiter warehouse
OQC Inspection
E-map
1
SCM confirm FG
status by OQC system
Jupiter confirm FG status by OQC system
①
②

## Slide 3
FA
E-map at FA warehouse
17
10 Pallets
10 Pallets
OK product
10 Pallets
10 Pallets
FA warehouse (Waiting Pallet ID)
5
Pallets
5
Pallets
FA warehouse
Waiting AQ2/NG FG)

## Slide 4
E-map at FA warehouse
17
Nội dung công việc:

## Slide 5
Rule to Judge 1 LOT
2
1st sample
2nd sample
N sample
……
OK
OK
OK
Final Judgment for Lot
OK
Identify 1 lot:
There is another model to insert running while current model is running  Switching model time is counted a new lot (Lot: Change another model or finish working shift)
If during FA running, happen NG nếu cần thiết thì OQC sẽ chia lot
Trong trường hợp OQC muốn gộp lô thì sẽ áp dụng tiêu chuẩn lô kết hợp (Lô kết hợp được tính trong trường hợp 1 model sản xuất liên tục của các ngày liền kề (thông thường là 1 tuần) và chất lượng phải ổn định)
Judgment 1 lot:
OQC will judge lot after finish inspection all sample Q'ty regardless of whether production has ended  Condition: OQC finish sample Q’ty + FA finish production + FA/OQC no happen NG
(Including Characteristic, Specification, Reliability sampling finished)

## Slide 6
Step 1: SCM send inventory & shipment plan
Step 2: FA update inventory & shipment plan
① Confirm shortage shipment
◆ Proposal
◆ Current
Indicate priority shipment model to announce OQC pick up inspection
Indicate details: Ship by Board/Air, Stock Q'ty, shipment Q’ty, Minus product compare vs shipment plan
Minus product: Q’ty, Reason, when re-running (need indicate)
In case production plan be changed  Auto refresh
Classify type of product and display : EMC, PP, PMP and can shipment or not (Ex: PP cannot shipment..)
Using time: 5 mins/day*4 BD/BU =20 mins/day
Save time: 20 mins/day
OQC confirm shipment plan to focus priority shipment models by manual
Step 3: OQC input shipment info to focus check priority
Request system will be displayed details:
3
IT confirm: Hưng Đạo sẽ trả lời về lấy dữ liệu hàng thiếu (SCM xác nhận tiếp)

## Slide 7
Step 2: OQC copy into OQC format to control
Step 1: PCS send Daily production plan <Email/Server>
① OQC re-make production plan
OQC re-making production base on information of PCS:
Add some information: Sample Q’ty, PL, Characteristic, Reliability, Specification…
 Using time: 10 mins/day
System will link with OQC inspection plan and auto update:
 Save time: 10 mins/day
OQC re-making production plan base on production plan that PCS send
◆ Proposal
◆ Current
OQC make database: Sample Q’ty; Reliability plan
System will be linked with OQC Inspection plan:
OQC sampling Q’ty (Incase if happen Quality issue, sample Q’ty level will be changed  Return to previous level  OQC make Data base)
Add : 1 column for adjust sample if need to follow up quality issue
Auto assign model that should be Reliability test
Auto change sample Q’ty level (Ex: Normal level  Loosen level)
If cannot catch up plan  Can adjust and display reason (Only OQC member can revise)
Indicate minus product in OQC control sheet
Q’ty sample Standard
Plan
Plan
4

## Slide 8
② OQC pick up sample
Scan barcode of Outer box  Displays Outer box OQC pick up: FA easy to control sample quantity OQC pick up (FA easy to inventory Q’ty)
System will remind OQC to pick up sample
Indicate time OQC pick up sample on system
Indicate pallet OQC pick up sample to eliminate finding and scan barcode many times
Using time: 1mins*8 times/day=8 mins/day
Save: 8 mins/day
OQC pick up sample follow serial range
◆ Proposal
◆ Current
Step 1: Access PSNV Portal to confirm Production result
Step 2: Divide serial range to pick up sample at Pallet
Pick up outer box & put indication
DP
Pick up inner box & put indication
DECT
System can be indicated:
5

## Slide 9
③ Reading barcode Inner/Outer 1st time
Using time: 30lots*10sec*2Outer boxes=10mins/day
Save: 10 mins/day
Confirm Outer carton and inner box
◆ Proposal
◆ Current
Reading Barcode of Outer box and Inner box
System link weight check system to confirm Outer box includes which inner boxes
6
Purpose: To confirm Outer box includes how many inner box and which serial No
Using result of FA weight check system  Eliminate operation at OQC

## Slide 10
④ Weight check 1st time
Using time: 150pcs*5sec*2 BD/BU=24mins/day
Save: 24 mins/day
Weight check offline at OQC to confirm accessory
◆ Proposal
◆ Current
Weight check 1st time (Control offline):
System link weight check system to weight of inner box
7
FA already applied weight check system: No need add this point  Eliminate weight check 1st at OQC
Purpose: To confirm full inner box before un-packing

## Slide 11
⑤ OQC Normal inspection
OQC normal inspection
◆ Proposal
◆ Current
OQC scan barcode serial No of product  Auto link with OQC checksheet
After OQC finish inspection  System indicate result of each serial No (In case NG will be indicated NG situation and reason NG)
System auto confirm matching sample Q’ty with database to indicate changing situation
+ System alarm if inspect duplicated serial No
+ Save history of sample check  Can Traceability
Incase FA happen quality issue  Alarm on system (Prevent OQC judgment OK when FA happen NG)  How to return product of this lot?
System link with Database sample Q’ty:
Appearance check
Function check
Confirm the number of samples to be taken
Manual confirm sample Q’ty enough or not
Current inspection procedure
8

## Slide 12
⑥ Reliability inspection
Reliability inspection:
◆ Proposal
◆ Current
OQC make Database about grouping series model need to check Characteristic, Reliability (Monthly)
System auto select model and remind to inspect:
+ Limit Q’ty of model to be suitable with OQC lead time
(Ex: OQC can check maximum 2pcs characteristic)
+ System default: After Reliability test  Normal inspection.
In case sample not yet checked normal  Will be alarm and
cannot judgment lot
+ In case happen Quality issue will be displayed NG situation
and after rework/repair  Change situation (Have history:
Main cause, action)
+ If model only produced 1 time in a month  Need to
indicate in inspection plan to remind OQC pick up
Basic function check: Power ON check
Inspect: Characteristic, Specification, Reliability
Confirm checking plan of characteristic, specification, reliability
Full function check
System link with Database sample Q’ty:
Indicate result in OQC control sheet
Current inspection procedure
9

## Slide 13
Reading barcode Product Inner to confirm correct S/N
⑦ Reading barcode Product Inner to confirm correct serial No
OQC make master list product ingredients: Monitor, camera, wireless, charger…
System can auto indicate ingredients must read barcode
This process is re-packing:
+ How to indicate set by set inspection result ?
NG or OK ? Any problem happen? What is next action ?
+ How this result link to total Judgment ?
Confirm ingredients of product for ensure matching Serial No
◆ Proposal
◆ Current
Reading barcode Product Inner to confirm correct S/N
10

## Slide 14
⑧ Weight check 2nd time
Current procedure from PCS  OQC  FA  SCM
◆ Proposal
◆ Current
Weight check 2nd time:
Purpose: To confirm full inner box after packing, compare weight check 1st time & 2nd time for judgment
Weight check 2nd time: Auto link with weight check system of FA to compare weight of inner box and Judgment
FA weight check system
Link
11
How can detect if FA weight check system have trouble ?

## Slide 15
⑨ Reading barcode Inner/Outer 2nd time
Confirm matching Outer box with inner box
◆ Proposal
◆ Current
Scan ID outer  Auto link with FA weight check to compare Outer box & inner box
Reading barcode Outer & Inner 2nd time
Purpose: Ensure correct Outer box & Inner box
System auto link with FA weight check system
FA weight check system
Link
12

## Slide 16
⑯ Output check sheet inspection & Report
 Using time: 10 mins/day
Save time: 10 mins/day
Record OQC inspection check sheet and report
◆ Proposal
◆ Current
System auto output: Production Q’ty, Serial range, FA line, Production date, OQC sample serial No, Inspection date, Sample Q’ty
When reading barcode to start inspection : System link and open OQC check sheet. Then OQC check 1pc complete and indicate OK  Link to system for inspection result
Auto output inspection check sheet (Pdf) follow inspection date, lot
System auto output OQC inspection result
Current situation:
Manual making OQC inspection check sheet:
Manual input summary OQC inspection result:
13

## Slide 17
⑪~⑮ OQC chop stamp
Current chop stamp procedure
Using time:
DP/Dect: 480 mins/day
MW/TV/PJ/SB/PAPVN: 480mins/day
Save time: 960 mins/day ~ 2pax
◆ Proposal
◆ Current
Indicate Judgment lot on system  All sections can understand lot situation
Eliminate physical chop stamp
How system link with ID pallet station or how to prevent production move to SCM without OQC approval: Using PDA to confirm Pallet situation, if OK  can transfer pallet
System auto indicate judgment lot
Current situation:
Finding pallet to confirm correct model, Q’ty
Read ID Pallet & S/N carton box by excel file
OQC find Pallet ID
Matching ID Pallet and Outer Carton
Find all same model, production date, line, shift
OQC chop stamp all ID Pallet
OQC
OK
DD-MM-YY
Chop stamp on Pallet sheet
14
2nd Floor: Đối với các pallet OQC đóng dấu thì FA sẽ kéo ra và để ở khu vực gần thang máy, nếu OK cả lô thì mới cho vào thang máy
1st Floor: Diện tích kho FA và SCM nhỏ

## Slide 18
OQC DASH BOARD
Visualize status of OQC inspection situation
Indication location at warehouse
OK
Checking
NG
Not checked yet
Checking
<Can move pallet>
Status situation
Not checked yet : OQC not taken sample yet
Checking : Under OQC checking
Checking : Under OQC checking (Sample Q’ty already checked over a half Q’ty of all sample)
<Can move pallet>
OK : All Lot judgment OK
NG : Lot judged NG
OQC inspection indication
Location indication at warehouse
15
1st Floor: How to control non-inspection pallet ?

## Slide 19
Preparation Equipment for system
16
Section | Name Equipment | Image | Function | Quantity
OQC | Tablet windows (Connect with barcode reader) or PDA |  | 1.1, Pick up sample 1.2, Return Sample 1.3, Find quickly Pallet ID and Model at FA & SCM area 1.4, Visualize OQC inspection with FA, SCM | 3 (FA transfer)
FA | PDA |  | 2.1, Verify OQC judgment 2.2, Check the status of OQC inspection | 3 (FA consider)
Equipment list require
Total Investment ($) | Efficiency/M ($) | Efficiency/Y ($) | ROI /Y
1,800 | 1,085 | 13,020 | 0.13824
ROI

## Slide 20
Currently
Manual check OQC display OK
Manual transfer F/G to SCS (SAP system)
Printing hard movement slip: 3600pcs/monthly  7.2Ream
Cost: 7.2*2.47$ = 17.78$/month ~ 213.4$/Year
Improvement
Check OQC OK by PDA
Auto transfer F/G to SCS (SAP system)
Abolish hard movement slip: 7.2Ream
Save Cost: 213.4$/Year
BEFORE
AFTER
FA
Reduced : 213.4 S/Y
Current process
Print movement slip
Manual check OQC OK
Production F/G OK
FA Make ID ID pallet
OQC stamping OK on slip sheet
Waiting OQC check
FA transfer SCS (SAP system)
FA transfer SCS (Actual)
OQC OK
Download ID pallet scaned
Print movement slip
Production F/G OK
FA Make ID ID pallet
OQC stamping OK on System
Waiting OQC check
Auto transfer
SCS (SAP system)
FA transfer SCS (Actual)
OQC OK
Download ID pallet scaned
Improvement process
OQC OK
Check OQC OK by PDA
LINK
SCS Receive the finish goods Scan ID Pallet Code
Change method transfer F/G to SCS
17

## Slide 21
OQC DIGITAL SYSTEM LINK WMS & CONFIRMATION DATA
DASHBOARD
SCS request:
Visualize status of model following shipment plan daily
Link final confirmation to WMS/PDA for operator working in warehouse
LINK WMS/PDA
FA
SCS
OQC
Finish production
Pallet ID finish
Judgement OK
Sampling inspection
Judgement OK
Scan ID pallet to receive
Confirm receiving
SCS check all data by download
**
Scan ID pallet
Email auto
Result NG
Confirm data PDA
FA/QC recheck
Shipment plan
*
②
①
Shipment plan
Result judged OK
③
*
**
③
Dashboard
PSNV Portal
“Control shipping plan”
WMS
Judgement auto email
FA transfer cargo to SCS
Option 1
Option 2
Warning to dashboard
SCS visualize on pallet
①
WMS
Dashboard
Confirm receiving
Format check
Auto update
SCM
18

## Slide 22
FORMAT DOWNLOAD FROM DASHBOARD
Details shortage shipment plan daily on WMS
Shortage shipment plan daily on WMS
OQC DIGITAL SYSTEM LINK WMS & CONFIRMATION DATA
19
SCM

## Slide 23
Control process sample at OQC area
Pick up sample
Reading barcode Inner/Outer excel file
Reading barcode
Inner/Outer excel file
Confirm S/N Outer & all inner boxes
Return sample
Weight check 1st
Weight check 2nd
Reliability
OQC
inspection
Numbering control & Separate area
Confirm S/N Outer & all inner boxes
Product / Warranty/ Manual & Inner box
Accessory control
Accessory control
Production Line
Warehouse FA
Reading BC
Product/Inner excel file
Improvement
No Link
No Link
No Link
No Link
No Link
No Link
No Link
Database server OQC
Auto link weight FA
Auto link weight FA
Control pick-up quantity
1
2
3
4
5
6
7
8
Steps
1
2
3
4
5
6
7
8
2
OQC inspection result no link FA & SCM system, easy mistake.
All procedures are manual by Excel, loss time to traceability, and skip processes.
The results of the inspection process are manually stamped. Loss of time to stamp.
OQC Visualize System

## Slide 24
E chop for OQC inspection
OQC member pick up sample
Shrink machine
OQC inspection
NG
OK
SCM area
FA fix location
FA shrink pallet ID
DECT area
OQC return sample
Use physical stamp
New system link FA-SCM-OQC
FA
OQC
SCM
Link
Link
Visualize OQC inspection
Visualize FA Warehouse area
OQC
OK
Day- Month- Year
E – chop can
replace
WMS system
Auto judgment OK for
All pallet ID the same Model, production date, line and shift.
SCM Out location
Shipping To market
Weight check
NG Location
SCM Warehouse
Steps
9
10
11
12
13
14
OQC
OK
Day- Month- Year
Database server
4
DP area
OQC Visualize System

## Slide 25
4
OQC Visualize System
FA
WMS
SCM warehouse
Combine F/G
Report S/N
(Export SI)
Shipment
OQC system
Function IT: SCM compare S/N, if 1 S/N not yet OK  Cannot shipment for all
c
OQC system
SCM warehouse
Shipment
Send email excel file to SCM: Pallet ID, Model, S/N
Jupiter
Function IT: SCM compare S/N, if 1 S/N not yet OK  Cannot shipment for all
c
Shipment to Market from SCM
Shipment to Market from Jupiter
Request:
IT : Auto indicate S/N OK or not
IT : Confirm with Hưng Đạo about Report S/N (SI)
IT : Add function of OQC for SCM

## Slide 26
4
OQC Visualize System
Nội dung họp 20-Dec-24
Update thông tin của các nội dung họp lần trước (6-Dec-24)
Thảo luận về việc khi đánh giá all lot trong OQC thì cách nhận diện kết thúc lot trên FA
Thảo luận về báo cáo xuất hàng bên Hưng Đạo và cập nhật hàng thiếu hàng ngày