## Slide 1
PQC – RoHS team
Move part into PQC-RoHS room to analyse
Confirm result OK/NG lot by click on website
1. Auto input the all data of part need check RoHS into SAP ( ZQV011,14,15,17** ) by click website.
2. Auto deduct Quantity on SAP after confirmed Quantity need take to test RoHS.
Non-inspection
Inspection
Inspection
Move other part into PQC room to inspection
Confirm result checked lot by Click OK/NG indicate on website
Open the drawing & WI on Tablet to direct inspection
Confirm part  Auto input the part situation on the system and start inspection by select part
Use tablet to confirm part need test alcohol, tape, function… by select part
Manual deduct Quantity on SAP and make Transfer report to MCS.
Normal inspection ( Non-issue out )
Reliability testing ( Issue out )
PQC – Inspection team
Scan GR
Separate non-inspection & inspection
MCS
MCS
PQC
-Get sample
-Or direct checking
by table
Activity 1: Electronic standardization of stamps for IQC departments
Control process get sample at IQC area
Inspection
Inspection
Inspection
Moving part to rack for Storing
MCS
Find Part OK / NG to storing
IQC chop stamp all lot
MCS Receiving Goods
MCS Fix location
IQC check & chop stamp
MCS Find OK /NG part
Step 5:Storing
Vendor
PQC
OK
Day- Month- Year
PQC
NG
Day- Month- Year
PQC
NG
Day- Month- Year
PQC
OK
Day- Month- Year
Fix
location
IQC chop stamp only one receiving card
NG
OK
OK

## Slide 2
Activity 1: Electronic standardization of stamps for IQC departments
Part incoming
Waiting area
OK / NG
Inspection Normal
Inspection ROHS
Test alcohol, tape, function
Chop stamp all lot
Chop stamp one receiving card
Not chop stamp
OK
OK / NG
OK / NG
Kho MCS OK
Kho NG
Storing
NG
Print part card
Scan barcode
Auto deduct Quantity on SAP
Loss time
Loss time
Kho MCS OK
IQC room
Inspection recheck
OK
Chop stamp
Loss time
Kho NG
Chop stamp
NG
Loss time
Part incoming
Kho SMT OK
Non inspection
IQC room
Inspection recheck
Chop stamp
Loss time
OK
Kho NG
Chop stamp
Loss time
NG
1. IQC Inspection & chop stamp procedure
2. IQC Inspection recheck, more 1 Year
3. IQC Inspection recheck SMT warehouse more 1 year
Chop stamp get sample
Loss time

## Slide 3
SWMS
IQC inspection
OK
NG
Activity 1: Electronic standardization of stamps for IQC departments
Improvement Stamp
IQC pick up sample
Non-inspection
Inspection
Inspection
PQC
OK
Day- Month- Year
MCS check status Inspection
No need stamp
PQC
Sampling
No need stamp
Storing
Warehouse MCS
OK
OK
OK
NG
QC Room
Recheck, more 1 Year
IQC inspection recheck
OK
NG
Print recheck card
OK
Store
Visualize Inspection IQC
MCS
IQC
IQC can traceability and export daily
MCS print Receiving card

## Slide 4
Activity 1: Electronic standardization of stamps for IQC departments
Summary Merit if IQC no chop stamp on actual Pallet & Box/ Hopper
Item | Detail | Unit | No | Before |  |  |  | After |  |  | 
 |  |  |  | PL part | Electric Part | Mecanical part | RoHS | PL part | Electric Part | Mecanical part | RoHS
Incoming lot | Average number of lots coming in a month (inspection) | Lot | (1) | 507 | 369 | 2681 | 960 | 507 | 369 | 2681 | 960
 | Average number of pallets / 1 Lot incoming | Palet | (2) | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
 | Average number of boxes, hoppers/ 1 Pallet | Box | (3) | 15 | 13 | 5 | 7 | 15 | 13 | 5 | 7
Time for chop stamp | Time to move and stamp OK/NG for 1 receiving card/1 Pallet (seconds) | Second | (4) | 10 | 10 | 10 | 10 |  |  |  | 
 | Time check stamp for 1 box (seconds) | Second | (5) | 10 | 5 | 5 | - |  |  |  | 
 | Date Code / Batch Time Record (seconds) | Second | (6) | 180 | 45 | 45 | - | 180 | 45 | 45 | -
 | Time to move to warehouse for return and stamping/ 1 Lot | Second | (7) | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120
 | Total time / Lot = (4*2)+(5*3*2)+(6) +(7) (second) | Second | (8) | 780 | 390 | 270 | 150 | 300 | 165 | 165 | 120
Total Time / month = 8*1 (Hours) |  | Second | (9) | 395,460 | 143,910 | 723,870 | 144,000 | 152,100 | 60,885 | 442,365 | 115,200
Different (Hours) |  | Hour |  | 391 |  |  |  | 214 |  |  | 
 |  |  |  | 177 |  |  |  |  |  |  | 
Final summary |  | 
Working time 1 pax / 1Month | 192 | Hours
Can save time if delete chop stamp | 177 | Hours
Save manpower / month | 0.92 | Pax

## Slide 5: Activity 2 : Link Weight Check System FA-SCM-OQC
Control process sample at OQC area
Pick up sample
Reading barcode Inner/Outer excel file
Reading barcode
Inner/Outer excel file
Confirm S/N Outer & all inner boxes
Return to Pallet
Weight check 1st
Weight check 2nd
Reliability
OQC
inspection
Numbering control & Separate area
Confirm S/N Outer & all inner boxes
Product / Warranty/ Manual & Inner box
Accessory control
Accessory control
Production Line
Warehouse FA
Database server
Reading BC
Product/Inner excel file
Warehouse FA
Reading BC inspection result by new software
Production Line
Confirm S/N Outer & all inner boxes
Accessory control
Get sample by Mobile
Scan barcode Inner/Outer by new software
Weight check 1st
OQC
inspection
Weight check 2nd
Numbering control & Separate area
Product / Warranty/ Manual & Inner box
Accessory control
Scan barcode Inner/Outer by new software
Return to Pallet by mobile
Confirm S/N Outer & all inner boxes
Reliability
Improvement
No Link
No Link
No Link
No Link
No Link
No Link
No Link

## Slide 6
Activity 2 : Link Weight Check System FA-SCM-OQC
E chop for OQC inspection
Line 2A
Line 1A
Line 3A
Line 4A
Line 5A
OQC member pick up sample
Weight check 1
Scan serial outer / inner the first
OQC inspection
Scan serial outer / inner the second
Weight check 2
Input inspection result on excel file
Shrink machine
OQC inspection result
OK
NG
NG
location
DP area
FA fix location
FA shrink pallet ID
DECT area
Matching ID Pallet and Outer Carton
OQC return sample
Recode ID Pallet & S/N carton box by excel file
OQC chop stamp all ID Pallet
Find all same model, production date, line, shift
OQC
OK
Day- Month- Year
OQC find Pallet ID
OQC Inspection
Chop stamp Process
New system link FA-SCM-OQC
FA
OQC
SCM
Link
Link
Visualize OQC inspection
Visualize FA Warehouse area
OQC
OK
Day- Month- Year
E – chop can
replace
WMS system
Auto judgment OK for
All pallet ID the same Model, production date, line and shift.
SCM Out location
Shipping To market
Production line
Database server
SCM Warehouse

## Slide 7
◆ After
OQC Issue
Risky point : Wrong packing pass to market by control offline
Loss time to confirm production result & Shipment schedule : 90sec*150 lots=3.75H/day.
2pax/ day need to follow chop stamp in warehouse.
Improvement: Link system from FA-OQC-SCM
Prevent wrong packing.
Save time : 3.75H/day ~ 990H/year
Save manpower : △ 2pax for stamp ~ 12K$/ year
◆Before
FA
OQC
SCM
No indicate shipment priority
No indicate result timely
Cannot use weight system  compare S/N by manual
Update OQC result not timely.
Loss time to come to SCM for chop stamp.
Loss time to confirm stamp by visual check
2pax
FA
OQC
SCM
Indicate result timely
Indicate shipment priority
Use weight system  auto compare S/N
Online update OQC result & Save time to come to SCM for chop stamp
No need check stamp by visual
Confirm OQC result by system
Target improve:
Prevent wrong packing leakage out to market
△ 2pax for stamp by manual
Link
Link
Activity 2: Link weight check system FA-SCM-OQC

## Slide 8
Note: In case the model have not Serial Number  They should be controlled as current method
FA
Shipment
- Save Weight Check Date
on server : Production
Date/Model/Q’ty
Pallet ID
SCM
① Add OQC :
Input sampling plan
Input Sampling product & Serial No
② Indication OQC situation:
Input Checking result
Input Final judgment All lot.
 Send result by Email auto
- Issue Pallet ID: Model/Q’ty/SN
- Issue Movement slip <SAP>
- Read Pallet ID Model/Q’ty
- Compare FG & WMS
- Read Pallet: <Model/Q’ty>
- Compare FG & WMS
③ QC inspection result:
Reading Pallet ID to check OQC result
Indicate OK lot
④ Function: If OQC judgment NG or Not yet
Stop next step
< PSNV/ Jupiter >
Study to link weight check & WMS
Save:
8,000min/month
Save:
Reduce 2pax
990H/year
Save:
4,000 min/month
CURRENT SITUATION
Additional
Additional
Additional
Additional
- Pick up sampling
inspection
REQUEST
MERIT
OQC
Activity 2: Link Weight Check System FA-SCM-OQC

## Slide 9
Issue Job And Schedule To Complete
 |  |  | 2024 |  |  |  |  |  | 2025 |  | 
No | Detail Function | Group Function | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar
1 | IQC Normal & ROHS inspection on website | E chop for IQC inspection |  |  |  |  |  |  |  |  | 
2 | IQC Normal & ROHS inspection on mobile |  |  |  |  |  |  |  |  |  | 
3 | IQC Recheck inspection on web & mobile |  |  |  |  |  |  |  |  |  | 
4 | IQC 1 Year inspection on web & mobile |  |  |  |  |  |  |  |  |  | 
5 | Show inspection status on mobile |  |  |  |  |  |  |  |  |  | 
6 | Find material location quickly on mobile |  |  |  |  |  |  |  |  |  | 
7 | Pick up & return sample for OQC | E chop for OQC inspection |  |  |  |  |  |  |  |  | 
8 | Compare serial outer & inner boxes |  |  |  |  |  |  |  |  |  | 
9 | Link weight OQC with weight FA |  |  |  |  |  |  |  |  |  | 
10 | Input checking OQC result auto judgment all lot for production result in day. |  |  |  |  |  |  |  |  |  | 
11 | Auto link inspection result OQC for SCM |  |  |  |  |  |  |  |  |  | 
12 | Visualize inspection result OQC,FA & SCM |  |  |  |  |  |  |  |  |  | 
Plan
Actual
Go-live