## Slide 1: K
Panasonic System Networks Vietnam
Information Systems Section
OQC DIGITAL SYSTEM

## Slide 2
OQC: Loss time to find and chop stamp.
FA loss of time to check stamps by appearance check
OQC manual control when picking up samples
FA does not control quantity of OQC pick-up
No indicate shipment priority
Manual control weight check
Update OQC result not timely
Each step is an independent, easy-skip process
Manual make report
SCM loss of time to confirm OQC inspection result to input WMS
WMS
Database OQC
FA create Pallet ID
Database Weight check
OQC
Pick sample
Return sample
FA In/Out location
Visualize OQC inspection result
OQC Judgement all lot
CURRENT
NEW SYSTEM
AFTER
System indicate S/N OQC pickup
Indicate models shipment priority
System indicate OQC & Lot judgment
Reduce manual job OQC
 Save: 1,000H/year
E-chop and indication on system
FA: Save 213.4$/year
OQC: ∆2pax
E-chop and indication on system
SCM: Save 800H/year
1
OQC inspection
OQC DIGITAL SYSTEM
Pick up simple
OQC Inspection
Chop stamp physical
Shipment
Software
Weight check
1
E-Map control
Shrink machine
FA, SCM warehouse
Visualize shipment priority, control quantity pickup

## Slide 3: OQC DIGITAL SYSTEM
Control process sample at OQC area
Pick up sample
Reading barcode Inner/Outer excel file
Reading barcode
Inner/Outer excel file
Confirm S/N Outer & all inner boxes
Return sample
Weight check 1st
Weight check 2nd
Reliability
OQC
inspection
Numbering control & Separate area
Confirm S/N Outer & all inner boxes
Product / Warranty/ Manual & Inner box
Accessory control
Accessory control
Production Line
Warehouse FA
Reading BC
Product/Inner excel file
Improvement
No Link
No Link
No Link
No Link
No Link
No Link
No Link
Database server OQC
Auto link weight FA
Auto link weight FA
Control pick-up quantity
1
2
3
4
5
6
7
8
Steps
1
2
3
4
5
6
7
8
2
OQC inspection result no link FA & SCM system, easy mistake.
All procedures are manual by Excel, loss time to traceability, and skip processes.
The results of the inspection process are manually stamped. Loss of time to stamp.

## Slide 4
OQC DIGITAL SYSTEM
E chop for OQC inspection
OQC member pick up sample
Shrink machine
OQC inspection
NG
OK
SCM area
FA fix location
FA shrink pallet ID
DECT area
OQC return sample
Use physical stamp
New system link FA-SCM-OQC
FA
OQC
SCM
Link
Link
Visualize OQC inspection
Visualize FA Warehouse area
OQC
OK
Day- Month- Year
E – chop can
replace
WMS system
Auto judgment OK for
All pallet ID the same Model, production date, line and shift.
SCM Out location
Shipping To market
Weight check
NG Location
SCM Warehouse
Steps
9
10
11
12
13
14
OQC
OK
Day- Month- Year
Database server
3
DP area

## Slide 5
Procurement activity
Section | Name Equipment | Image | Function | Quantity
OQC | Tablet windows (Connect with barcode reader) |  | 1.1 Pick up sample 1.2 Return Sample 1.3 Find quickly Pallet ID and Model at FA & SCM area 1.4 Visualize OQC inspection with FA, SCM | 3
FA | Mobile device |  | 2.1 Fix in & fix out location 2.2 Check the status of the OQC inspection | 2
OQC DIGITAL SYSTEM
4
Equipment list require

## Slide 6
Plan
Actual
Go-live
OQC DIGITAL SYSTEM
5
Project Schedule
Group Function | Department | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar
Meeting, discuss, analyze | SCM/QC/FA/IT |  |  |  |  |  |  |  | 
Upload plan, Pick-up sample | SCM/QC/FA/IT |  |  |  |  |  |  |  | 
Confirm Outer carton and inner box | QC/IT |  |  |  |  |  |  |  | 
Modify weight check OQC | QC/IT |  |  |  |  |  |  |  | 
OQC inspection & judgment all lots | SCM/QC/FA/IT |  |  |  |  |  |  |  | 
Visualize inspection result OQC | -SCM/QC/FA/IT |  |  |  |  |  |  |  | 
Report daily OQC | QC/IT |  |  |  |  |  |  |  | 

## Slide 7
Step 1: SCM send inventory & shipment plan
Step 2: FA update inventory & shipment plan
◆ Proposal
◆ Current
Indicate priority shipment model to announce OQC pick up inspection
Indicate details: Ship by Board/Air, Stock Q'ty, shipment Q’ty, Minus product compare vs shipment plan
Minus product: Q’ty, Reason, when re-running (need indicate)
In case production plan be changed  Auto refresh
Classify type of product and display : EMC, PP, PMP and can shipment or not (Ex: PP cannot shipment..)
Using time: 5 mins/day*4 BD/BU =20 mins/day
Save time: 20 mins/day
OQC confirm shipment plan to focus priority shipment models by manual
Step 3: OQC input shipment info to focus check priority
Request system will be displayed details:
5
OQC DIGITAL SYSTEM
6

## Slide 8
Step 2: OQC copy into OQC format to control
Step 1: PCS send Daily production plan <Email/Server>
OQC re-making production base on information of PCS:
Add some information: Sample Q’ty, PL, Characteristic, Reliability, Specification…
 Using time: 10 mins/day
System will link with OQC inspection plan and auto update:
 Save time: 10 mins/day
OQC re-making production plan base on production plan that PCS send
◆ Proposal
◆ Current
OQC make database: Sample Q’ty; Reliability plan
System will be linked with OQC Inspection plan:
OQC sampling Q’ty (Incase if happen Quality issue, sample Q’ty level will be changed  Return to previous level  OQC make Data base)
Add : 1 column for adjust sample if need to follow up quality issue
Auto assign model that should be Reliability test
Auto change sample Q’ty level (Ex: Normal level  Loosen level)
If cannot catch up plan  Can adjust and display reason (Only OQC member can revise)
Q’ty sample Standard
Plan
Plan
6
OQC DIGITAL SYSTEM
7

## Slide 9
Scan barcode of Outer box  Displays Outer box OQC pick up: FA easy to control sample quantity OQC pick up
System will remind OQC to pick up sample
Indicate time OQC pick up sample on system
Indicate pallet OQC pick up sample to eliminate finding and scan barcode many times
Using time: 1mins*8 times/day=8 mins/day
Save: 8 mins/day
OQC pick up sample follow serial range
◆ Proposal
◆ Current
Step 1: Access PSNV Portal to confirm Production result
Step 2: Divide serial range to pick up sample at Pallet
Pick up outer box & put indication
DP
Pick up inner box & put indication
DECT
System can be indicated:
7
OQC DIGITAL SYSTEM
8

## Slide 10
Using time: 30lots*10sec*2Outer boxes=10mins/day
Save: 10 mins/day
Reading barcode Inner/Outer 1st time
◆ Proposal
◆ Current
Reading Barcode of Outer box and Inner box
System link weight check system to confirm Outer box includes which inner boxes
8
Purpose: To confirm Outer box includes how many inner box and which serial No
OQC DIGITAL SYSTEM
9

## Slide 11
Using time: 150pcs*5sec*2 BD/BU=24mins/day
Save: 24 mins/day
Weight check 1st time offline at OQC to confirm accessory
◆ Proposal
◆ Current
Weight check 1st time (Control offline):
System link weight check system to weight of inner box
9
FA already applied weight check system: No need add this point  No need do weight check 1st at OQC
Purpose: To confirm full inner box before un-packing
OQC DIGITAL SYSTEM
10

## Slide 12
OQC normal inspection
◆ Proposal
◆ Current
After OQC finish inspection  System indicate result of each serial No (In case NG will be indicated NG situation and reason NG)
System auto confirm matching sample Q’ty with database to indicate changing situation
+ System alarm if inspect duplicated serial No
+ Save history of sample check  Can Traceability
Incase FA happen quality issue  How to indication on system (Prevent OQC judgment OK when FA happen NG)  How to return product of this lot?
System link with Database sample Q’ty:
Appearance check
Function check
Confirm the number of samples to be taken
Manual confirm sample Q’ty enough or not
Current inspection procedure
10
OQC DIGITAL SYSTEM
11

## Slide 13
Reliability inspection:
◆ Proposal
◆ Current
OQC make Database about grouping series model need to check Characteristic, Reliability (Monthly)
System auto select model and remind to inspect:
+ Limit Q’ty of model to be suitable with OQC lead time
(For Ex: OQC can check 2pcs characteristic)
+ System default: After Reliability test  Normal inspection.
In case sample not yet checked normal  Will be alarm
+ In case happen Quality issue will be displayed NG situation
and after rework/repair  Change situation (Have history:
Main cause, action)
+ If the model only produced 1 time in a month  Need to
indicate in inspection plan
Basic function check: Power ON check
Inspect: Characteristic, Specification, Reliability
Confirm checking plan of characteristic, specification, reliability
Full function check
System link with Database sample Q’ty:
Indicate result in OQC control sheet
Current inspection procedure
11
OQC DIGITAL SYSTEM
12

## Slide 14
Reading barcode Product Inner to confirm correct S/N
OQC make master list product ingredients: Monitor, camera, wireless, charger…
System can auto indicate ingredients must read barcode
Link with FA system to confirm ingredients inside?
This process is re-packing:
+ How to indicate set by set inspection result ?
NG or OK ? Any problem happen ?What is next action ?
+ How this result link to total Judgment ?
Reading barcode Product Inner to confirm correct serial No
◆ Proposal
◆ Current
Reading barcode Product Inner to confirm correct S/N
12
OQC DIGITAL SYSTEM
13

## Slide 15
Weight check 2nd time
◆ Proposal
◆ Current
Weight check 2nd time:
Purpose: To confirm full inner box after packing, compare weight check 1st time & 2nd time for judgment
Weight check 2nd time: Auto link with weight check system of FA to compare weight of inner box and Judgment
FA weight check system
Link
13
How can detect if FA weight check system have trouble ?
OQC DIGITAL SYSTEM
14

## Slide 16
Reading barcode Inner/Outer 2nd time to Confirm matching Outer box with inner box
◆ Proposal
◆ Current
Scan ID outer  Auto link with FA weight check to compare Outer box & inner box
Reading barcode Outer & Inner 2nd time
Purpose: Ensure correct Outer box & Inner box
System auto link with FA weight check system
FA weight check system
Link
14
OQC DIGITAL SYSTEM
15

## Slide 17
 Using time: 10 mins/day
Save time: 10 mins/day
Record OQC inspection check sheet and report
◆ Proposal
◆ Current
System auto output: Production Q’ty, Serial range, FA line, Production date, OQC sample serial No, Inspection date, Sample Q’ty
When reading barcode to start inspection : System link and open OQC check sheet. Then OQC check 1pc complete and indicate OK  Link to system for inspection result
System auto output OQC inspection result
Current situation:
Manual making OQC inspection check sheet:
Manual input summary OQC inspection result:
15
OQC DIGITAL SYSTEM
16

## Slide 18
Current chop stamp procedure
Using time:
DP/Dect: 480 mins/day
MW/TV/PJ/SB/PAPVN: 480mins/day
Save time: 960 mins/day ~ 2pax
◆ Proposal
◆ Current
Indicate Judgment lot on system  All sections can understand lot situation
Eliminate physical chop stamp
How system link with ID pallet station or how to prevent production move to SCM without OQC approval ?
System auto indicate judgment lot
Current situation:
Finding pallet to confirm correct model, Q’ty
Read ID Pallet & S/N carton box by excel file
OQC find Pallet ID
Matching ID Pallet and Outer Carton
Find all same model, production date, line, shift
OQC chop stamp all ID Pallet
OQC
OK
DD-MM-YY
Chop stamp on Pallet sheet
16
OQC DIGITAL SYSTEM
17

## Slide 19
OQC DIGITAL SYSTEM
Rule to Judge 1 LOT
Define 1 lot:
When a model runs, another model inserted will be counted as 1 lot. (Lot: when a new model is inserted or finishes a working shift)
Judgment 1 lot:
OQC will judge a lot after finishing the inspection of all sample quantities even though the production result is not finished yes.
1st sample
2nd sample
N sample
……
OK
OK
OK
Final Judgment for Lot
OK
18

## Slide 20
Visualize status of Lot
Indication location at warehouse
OK
Checking
NG
Not checked yet
Checking
<Can move pallet>
Status situation
Not checked yet : OQC not taken sample yet
Checking : Under OQC checking
Checking : Under OQC checking (Sample Q’ty already checked over a half Q’ty of all sample)
<Can move pallet>
OK : All Lot judgment OK
NG : Lot judged NG
OQC inspection indication
Location indication at warehouse
15
OQC DIGITAL SYSTEM
19

## Slide 21
Currently
Manual check OQC display OK
Manual transfer F/G to SCS (SAP system)
Printing hard movement slip: 3600pcs/monthly  7.2Ream
Cost: 7.2*2.47$ = 17.78$/month ~ 213.4$/Year
Improvement
Check OQC OK by PDA
Auto transfer F/G to SCS (SAP system)
Abolish hard movement slip: 7.2Ream
Save Cost: 213.4$/Year
BEFORE
AFTER
FA
Reduced : 213.4 S/Y
Current process
Print movement slip
Manual check OQC OK
Production F/G OK
FA Make ID ID pallet
OQC stamping OK on slip sheet
Waiting OQC check
FA transfer SCS (SAP system)
FA transfer SCS (Actual)
OQC OK
Download ID pallet scaned
Print movement slip
Production F/G OK
FA Make ID ID pallet
OQC stamping OK on System
Waiting OQC check
Auto transfer
SCS (SAP system)
FA transfer SCS (Actual)
OQC OK
Download ID pallet scaned
Improvement process
OQC OK
Check OQC OK by PDA
LINK
SCS Receive the finish goods Scan ID Pallet Code
Change method transfer F/G to SCS
20

## Slide 22
OQC DIGITAL SYSTEM LINK WMS & CONFIRMATION DATA
DASHBOARD
SCS request:
Visualize status of model following shipment plan daily
Link final confirmation to WMS/PDA for operator working in warehouse
LINK WMS/PDA
FA
SCS
OQC
Finish production
Pallet ID finish
Judgement OK
Sampling inspection
Judgement OK
Scan ID pallet to receive
Confirm receiving
SCS check all data by download
**
Scan ID pallet
Email auto
Result NG
Confirm data PDA
FA/QC recheck
Shipment plan
*
②
①
Shipment plan
Result judged OK
③
*
**
③
Dashboard
PSNV Portal
“Control shipping plan”
WMS
Judgement auto email
FA transfer cargo to SCS
Option 1
Option 2
Warning to dashboard
SCS visualize on pallet
①
WMS
Dashboard
Confirm receiving
Format check
Auto update
SCM
21

## Slide 23
FORMAT DOWNLOAD FROM DASHBOARD
Details shortage shipment plan daily on WMS
Shortage shipment plan daily on WMS
OQC DIGITAL SYSTEM LINK WMS & CONFIRMATION DATA
22
SCM

## Slide 24
OQC DIGITAL SYSTEM
Make Planning
SCM
FA
Send file inventory & shipment plan
Compare Stock base on file plan and update
OQC
Pick up sample to Inspection
Step 1
OQC
Step 2
OQC
Scan barcode outer serial
Scan all barcodes inner serial
Confirm S/N Outer & all inner boxes
Based on sample standard file
Input daily production to excel file
Filter priority shipmen models to inspection
Based on the production plan file of SCM
Pick up samples based on weight check system results
Analysis of OQC System Functional Diagram
Send daily production plan
PCS

## Slide 25
OQC DIGITAL SYSTEM
Step 3
OQC
Weight check 1st
Product weight control
Step 4
OQC
OQC
inspection
Normal inspection
Reliability inspection
Appearance inspection, function, WI
Characteristic, Vibration, Drop, Temperature test
Step 5
OQC
Scan barcode inner product
Based on the mater list
Analysis of OQC System Functional Diagram

## Slide 26
OQC DIGITAL SYSTEM
Step 6
OQC
Weight check 2nd
Product weight control
Step 7
OQC
Scan barcode outer serial
Scan all barcodes inner serial
Confirm S/N Outer & all inner boxes
Step 8
OQC
Return sample
Judgment all Lot
Analysis of OQC System Functional Diagram

## Slide 27
OQC DIGITAL SYSTEM
OK
OQC Inspection
ID Pallet Station
Packing FA
OQC get sample
FA warehouse
Case 1
SCM warehouse
Case 2
FA shrink Pallet ID
OQC Inspection
Find & Return correct Pallet ID taken
Return sample
OQC get sample
Find Pallet ID & FG
Find all lots same model, date, line, shift
Chop stamp physical all lots
OK
ID Pallet issue in FA process
return sample
None Pallet
NO ID Pallet
Notify NG error for FA
NG
NG
Chop stamp process of OQC
9
11
Record Pallet ID & SN carton by excel
Matching ID Pallet and Outer carton before return
Report daily by excel
12
13
14
10
9

## Slide 28
No | Items | Dept | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar
1 | Meeting, discuss, analyze | SCM/QC/FA/IT |  |  |  |  |  |  |  | 
2 | Confirm shortage shipment | SCM/QC/IT |  |  |  |  |  |  |  | 
3 | Upload production plan | SCM/QC/IT |  |  |  |  |  |  |  | 
4 | Pick-up sample | QC/IT |  |  |  |  |  |  |  | 
5 | Confirm Outer carton and inner box | QC/IT |  |  |  |  |  |  |  | 
6 | Modify weight check OQC | QC/IT |  |  |  |  |  |  |  | 
7 | OQC normal inspection | QC/IT |  |  |  |  |  |  |  | 
8 | OQC Reliability inspection | QC/IT |  |  |  |  |  |  |  | 
9 | Confirm all serial of product for ensure matching serial No | QC/IT |  |  |  |  |  |  |  | 
10 | Return sample | QC/IT |  |  |  |  |  |  |  | 
11 | Function OQC judgment all lot for production result | MCS |  |  |  |  |  |  |  | 
12 | Visualize inspection result OQC for FA | PMD |  |  |  |  |  |  |  | 
13 | Visualize inspection result OQC for SCM | PMD |  |  |  |  |  |  |  | 
14 | Visualize inspection result OQC with WMS of SCM | FA |  |  |  |  |  |  |  | 
15 | Report daily OQC | SCM |  |  |  |  |  |  |  | 
Plan
Actual
Go-live
OQC DIGITAL SYSTEM
Schedule OQC Digital System