## Slide 1: Request modify weight check system (DP, DECT, SB, Service)
BEFORE
AFTER
Base
Serial carton
① No verify matching serial product & serial carton
① Add verify serial product & serial carton
Only scan serial No on Carton box
Risk: Wrong mixing serial product & carton
Scan all serial product & carton box
Merit: ensure inner & outer matching
Remote
Carton
② No verify weight of big carton box
Only weight check single products
Risk: Missing products inside big carton box
② Add verify weight of big carton box
Verify weight of each products & total big carton
Merit: no missing products inside
③ Manual confirm leaflet, book by excel file
③ Add software confirm – link to weight check
Only confirm by excel file
Risk: loss record file, can not traceability
Confirm by software, link to weight check
Merit: traceability system
Weigh Product
No weigh total carton
Weigh Product
Weigh total carton
Apply: DP,DECT
Apply: SB, Service
Apply: DP, DECT, SB

## Slide 2
Summary Weight check system all category
① Verify matching serial inner product & serial outer carton
 | TV | DP | DECT | SB | MW | PJ | Service
Weight check | O |  |  | O | O | O | Don’t have product serial
Excel file |  | O | O |  |  |  | 
Base
Remote
Carton
Need Add
Need Add
OK
OK
OK
OK
② Confirm leaflet, manual book
 | TV | DP | DECT | SB | MW | PJ | Service
Leaflet, book | Have | Have | Have | Have | Have | Have | None
Software | O |  |  |  | O | O | 
Excel |  | O | O | O |  |  | 
Need Soft
OK
OK
OK
OK
Need Soft
Need Soft
Scan on software
OK

## Slide 3
Activity 1 : Verify matching serial inner product & serial outer carton for weight DECT PHONE
【 Current Situation 】
No verify matching serial product & serial carton. Check compare serial by manual (Lost time : 3s/1pcs ~60min/day)
【Improvement 】
Add step verify serial product & serial carton (Reduce time : 20min/day ~ 5,760min/year -> Save : 132USD/year)
FCT
Assemble
Auto Inspection
Auto
Shipping
PL check
Fold box
Packing
Weight check
Stick serial no label in
Base & remote.
Compare serial carton with Base & remote
by manual. Because the serial no have barcode
Serial Base
No barcode
Serial remote
no barcode
KX-TGC1611SPC
4ECCJ170833
Scan barcode in Weight
Only scan serial No on Carton box
Base
Remote
Serial Carton
Current Issued
Improvement
FCT
Assemble
Auto Inspection
Auto
Shipping
PL check
Packing
Fold box
Stick serial label in
Base & remote.
Rick: Wrong mixing serial product & carton
Ricky process: mixing serial base an remote
3ABCB001005
3ABCB001005
3ABCB001005
3ABCB001005
3ABCB001005
3ABCB001005
Add QR Base
Add barcode remote
Wrong serial
Weight link to data base
Matching serial outer carton with serial base, handset.
Ensure quality ( Prevent mixing inner & outer serial )
NG, serial not matching
Alarm
Notes: PART BODY WIP using for 18L Model need 6 process include 5 process using press machine & process number 5 using bending machine but THANHCONG don’t have bending machine so need to order outside bending maker & back to THANHCONG and complete process number 6
-> take time to movement and high cost, difficult control
After study design bending tooling can use in press machine to replace using bending machine

## Slide 4
Activity 2 : Compare carton serial & product leaflet, book by Weight check for category DP, DECT, SOUND BIZ
【 Current Situation 】
Manual confirm leaflet, book by excel file -> can not traceability
【Improvement 】
Add software confirm – link to weight check
Current Issued
Improvement
No Link
Only confirm by excel file
Weight check
Scan serial leaflet , book
Risk: loss record file, can not traceability, mixing serial.
Database server
Weight check
Software
Scan serial leaflet , book
Detect wrong serial leaflet, book.
Can traceability system.
Notes: PART BODY WIP using for 18L Model need 6 process include 5 process using press machine & process number 5 using bending machine but THANHCONG don’t have bending machine so need to order outside bending maker & back to THANHCONG and complete process number 6
-> take time to movement and high cost, difficult control
After study design bending tooling can use in press machine to replace using bending machine

## Slide 5: Activity 3 : Add step verify to check serials all of products for cate DP
Improvement Activity [Prevent Human mistake]
Problem
Don’t have item to check serial number all of products
Action
Make verify link with excel file to detect if wrong S/N
Scan S/N on product by manual
Weight check did not detected
Wrong serial camera, wireless, warranty card
2,552g
Pair S/N
Packing
Assemble
PL
F1
F2
F3
F5
F4
Automation line
Weight check
Happened wrong s/n
Passed
Scan serial number by excel file
Total: DP: 10 lines / 272 models, DECT: 8 lines / 340 models
MW: 3 lines / 110 models, PJ-SB: 8 lines / 200 models
Weight check soft can detect if wrong serial no
Notify
Wrong serial number
Please, recheck again
OK
Alarm
Link to weight check
Weight link to data base
3ABCB001005
3ABCB001005
3ABCB001005
3ABCB001005
3ABCB001005
3ABCB001005
Wrong serial
Manual check S/N all of products

## Slide 6: Activity 4 : Link weight check system FA-SCM-OQC
Control process sample at OQC area
Pick up sample
Reading barcode Inner/Outer excel file
Reading barcode
Inner/Outer excel file
Confirm S/N Outer & all inner boxes
Return to Pallet
Weight check 1st
Weight check 2nd
Reliability
OQC
inspection
Numbering control & Separate area
Confirm S/N Outer & all inner boxes
Product / Warranty/ Manual & Inner box
Accessory control
Accessory control
Production Line
Warehouse FA
Database server
Reading BC
Product/Inner excel file
Warehouse FA
Reading BC inspection result by new software
Production Line
Confirm S/N Outer & all inner boxes
Accessory control
Get sample by Mobile
Scan barcode Inner/Outer by new software
Weight check 1st
OQC
inspection
Weight check 2nd
Numbering control & Separate area
Product / Warranty/ Manual & Inner box
Accessory control
Scan barcode Inner/Outer by new software
Return to Pallet by mobile
Confirm S/N Outer & all inner boxes
Reliability
Improvement
No Link
No Link
No Link
No Link
No Link
No Link
No Link

## Slide 7
Activity 4 : Link weight check system FA-SCM-OQC
E chop for OQC inspection
Line 2A
Line 1A
Line 3A
Line 4A
Line 5A
OQC member pick up sample
Weight check 1
Scan serial outer / inner the first
OQC inspection
Scan serial outer / inner the second
Weight check 2
Input inspection result on excel file
Shrink machine
OQC inspection result
OK
NG
NG
location
DP area
FA fix location
FA
DECT area
Matching ID Pallet and Outer Carton
OQC return sample
Recode ID Pallet & S/N carton box by excel file
OQC chop stamp all ID Pallet
Find all same model, production date, line, shift
OQC
OK
Day- Month- Year
OQC find Pallet ID
OQC Inspection
E-chop Process
New system link FA-SCM-OQC
FA
OQC
SCM
Link
Link
Visualize OQC inspection
Visualize FA Warehouse area
OQC
OK
Day- Month- Year
E – chop can
replace
Database server
Auto judgment OK for
All pallet ID the same Model, production date, line and shift.
SCM Out location
Shipping To market
Production line

## Slide 8
◆ After
OQC Issue
Risky point : Wrong packing pass to market by control offline
Loss time to confirm production result & Shipment schedule : 90sec*150 lots=3.75H/day.
2pax/ day need to follow chop stamp in warehouse.
Improvement: Link system from FA-OQC-SCM
Prevent wrong packing.
Save time : 3.75H/day ~ 990H/year
Save manpower : △ 2pax for stamp ~ 12K$/ year
◆Before
FA
OQC
SCM
No indicate shipment priority
No indicate result timely
Cannot use weight system  compare S/N by manual
Update OQC result not timely.
Loss time to come to SCM for chop stamp.
Loss time to confirm stamp by visual check
2pax
FA
OQC
SCM
Indicate result timely
Indicate shipment priority
Use weight system  auto compare S/N
Online update OQC result & Save time to come to SCM for chop stamp
No need check stamp by visual
Confirm OQC result by system
Target improve:
Prevent wrong packing leakage out to market
△ 2pax for stamp by manual
Link
Link
Project: Link weight check system FA-SCM-OQC

## Slide 9
Note: In case the model have not Serial Number  They should be controlled as current method
FA
Shipment
- Save Weight Check Date
on server : Production
Date/Model/Q’ty
Pallet ID
SCM
① Add OQC :
Input sampling plan
Input Sampling product & Serial No
② Indication OQC situation:
Input Checking result
Input Final judgment All lot.
 Send result by Email auto
- Issue Pallet ID: Model/Q’ty/SN
- Issue Movement slip <SAP>
- Read Pallet ID Model/Q’ty
- Compare FG & WMS
- Read Pallet: <Model/Q’ty>
- Compare FG & WMS
③ QC inspection result:
Reading Pallet ID to check OQC result
Indicate OK lot
④ Function: If OQC judgment NG or Not yet
Stop next step
< PSNV/ Jupiter >
Study to link weight check & WMS
Save:
8,000min/month
Save:
Reduce 2pax
990H/year
Save:
4,000 min/month
CURRENT SITUATION
Additional
Additional
Additional
Additional
- Pick up sampling
inspection
REQUEST
MERIT
OQC
Project: Link Weight Check System FA-SCM-OQC

## Slide 10
4HACG104436